## Slide 1: Distributed Logistics in an Urban Setting Using Small Unmanned Aerial Vehicles
Team Lakshya-IISc
Faculty Advisors:
Prof. Ranjan Ganguli
Prof. Dineshkumar Harursampath
Dr. S N Omkar
Department of Aerospace Engineering
Indian Institute of Science, Bangalore-560012

## Slide 2: Problem Statement for Graduate Teams
Overall concept of operations

## Slide 3: Problem Statement for Graduate Teams
Payload information
90% payload volume: 12 X 12 X 16 cubic inches
External slung load delivery for larger shipments

## Slide 4: Cargo, Customers & Shipments
Even distribution of customer locations
5000 packages per day in 10 hours delivery time
Shipment within 120 minutes
Uniformly random fashion of request from customers within first 8 hours

## Slide 5: System design questions
More than 1 vehicle design?
Maximum payload and range of each vehicle design?
Operating locations (FSL) other than Central Warehouse? Role?
RUAV automation technology required for “delivery to the door”?
Hybrid propulsion or power source or power augmentation?
Design for repair vs. design for inexpensive part replacement?
Acquisition, and operating cost of RUAVs for 3 years.

## Slide 6: Data Deliverables
Proposed concept of operations
Detailed performance analysis of the designed RUAV
General description of the RUAV with 3-view drawings of major components
Mission performance summary: flight speed, energy consumed, power required
Detailed weight statement of the RUAVs with analysis
Turnaround timeline & lifecycle cost estimate
Probability of package delivery in 2 hours
Prediction of acoustic signature of the RUAVs as per FAA flyover rules

## Slide 7: Measures of Effectiveness
System acquisition and yearly operating costs
Number of packages delivered per vehicle per day
Number of shipments with delivery time > 90 minutes
Pounds of CO2 emitted/delivery mile flown (daily average)
% of shipments delivered successfully

## Slide 8: Concept of Operation
Delivery area divided into (at least) 5 zones; with one FSL in each zone
FSLs – acts as the nodal point for each zone - temporary storage location for most likely packages for particular zone - transit point; refueling/recharging station; maintenance/repair, etc.

## Slide 9: Concept of Operation
Two RUAV designs considered: 1. Helicopter – heavier packages; transport packages from CW to FSL 2. Quad-copter – for lighter packages; delivers packages to customer location
Helicopter: advanced configuration based on Yamaha R-MAX design modified to suit the mission requirements for the SDC

## Slide 10: Yamaha R-MAX RUAV
Cruise speed ~ 20 km/hr
Endurance ~ 1 hour
Specification | Value
Main rotor diameter | 3115 mm
Tail rotor diameter | 545 mm
Number of blades | 2
Empty weight + fuel | 64 kg
Payload capacity | 30 kg
Engine output | 15.4 KW
Overall length | 3630 mm
Overall height | 1080 mm
Overall width | 720 mm

## Slide 11: Performance Analysis
Selection of baseline helicopter based on mission requirements: Yamaha R-MAX
Helicopter design objective:
Efficient hover performance
Efficient forward flight (cruise speed) performance
Taguchi method of robust design methodology for main rotor design
Design parameters:
Main rotor blade length
Plan-form variation (blade taper)
Rotor speed
Span-wise distribution of blade pre-twist

## Slide 12: Performance Analysis
Result of robust design using Taguchi method for hover performance:
Main rotor radius: 1.75 m
Rotor speed : 800 rpm
Blade plan-form : Tip chord length = 0.08 m Root chord length = 0.12 m
Blade pre-twist : 10 degrees

## Slide 13: Future Work
Robust design for forward flight (cruise speed of Yamaha R-MAX)
Associated ANOVA studies
Detailed performance analysis of modified R-MAX configuration: - performance studies for main rotor - power requirements of tail rotor - total power estimate considering drag due to fuselage, slung load, etc.

## Slide 14
Thank You

## Slide 15
Draft paper
Timeline
9 February
03 March
03 April
03 May 2015
29 May 2015
October 2015
Draft paper for AHS Forum 2016 and AIAA 2016 conferences
October 2015
First draft of Final Proposal
03 May 2015
Hardware Validation
(Pre-test predictions) Submission
03 April 2015
Letter of Intent
9 Feb 2015
Begins: Final Draft report
Demonstration of single (or multiple)
RUAV following an optimal path.
Additive manufacturing: 3D printing
Phase 5 Here
GPS based RUAV tracking
Phase 4 Here
Optimal Path Planning Algorithm
Phase 3 Here
RUAV Performance Analysis
Phase 2 Here
Hardware validation
Begins
Design Specs
Phase 1 Here
Timeline
Final Submission:
1) Final Proposal;
2) Executive Summary
3) Demonstration of hardware validation (video file)
29 May 2015
Extended draft paper for Journal
December 2015
Design Specs
Project delegation
RUAV Performance Analysis
RUAV Structural Analysis
Path Planning Algorithm